## Slide 1: 1024-bit vector register
A 1024-bit register is just a long row of bits
It contains many smaller numbers packed next to each other

## Slide 2: How numbers are stored
[ bits of int 0 ][ bits of int 1 ][ bits of int 2 ] ... [ bits of int 30 ][ bits of int 31 ]
Each block = 32 bits = one integer
All blocks together = 1024 bits

## Slide 3: Two input registers
Register A:
[A0][A1][A2] ... [A31]
Register B:
[B0][B1][B2] ... [B31]
Each [AX] or [BX] = 32-bit integer

## Slide 4: Vector addition
One vector ADD instruction:
[A0][A1][A2] ... [A31]
+
[B0][B1][B2] ... [B31]
=
[C0][C1][C2] ... [C31]
All additions happen at the same time.
Instead of doing:
for i in range(32):
c[i] = a[i] + b[i]

## Slide 5: Key idea
The big register is NOT one big number
It is many small numbers placed side by side
Vectorization = processing all of them at once
Of course, doing one addition between two 32-bit registers is faster than doing one addition between two 1024-bit registers. However, doing 32 32-bit registers additions is slower than 1 1024-bit register addition.

## Slide 6: CPU VS GPU
This is called VECTORIZATION.
This happens in your CPU.
It’s SIMD (Single Instruction Multiple Data).
Your GPU is NOT just that but with super big registers.
It’s actually something a little bit different called SIMT (Single Instruction Multiple Threads).
But that’s the same IDEA.